## Slide 1
DEMO DAM · DIGITAL TWIN
How It Works
The model, the equations, and every constant behind the dashboard
A technical walkthrough of the simulation layer: three operator inputs drive six sensor responses, one risk decomposition, and three scripted scenarios — all as pure, deterministic functions.
3
Sim inputs
6
Sensor nodes
2
Core equations
3
Scenarios
SU YAPI Engineering & Consulting · Para Sidara
Demonstration dataset — figures are simulated, not live field telemetry.

## Slide 2
What this deck covers
Four questions, answered in order. Skip to the one you need.
1 · How does data flow?
Three slider inputs → pure functions → sensors, risk, protocol, 3D twin. No hidden state, no server.
2 · How is each sensor reading calculated?
One linear superposition equation with per-sensor sensitivity coefficients. Slides 5–9.
3 · How is the risk score calculated?
Three weighted drivers plus a baseline, clamped and banded into three status levels. Slides 10–12.
4 · How do the scripted scenarios run?
Keyframe interpolation on a smoothstep curve, with events fired at progress thresholds. Slides 13–15.
5 · What is this model NOT?
The honest limits — what a reviewer should know before reading anything into the numbers. Slide 17.
Every constant in this deck is transcribed from src/lib/damModel.ts.

## Slide 3
1 · Data flow
One direction, top to bottom. Everything downstream is derived on render.
INPUTS
surge · pga · spillwayGate
Set by sliders, or driven by a running scenario.
PURE FUNCTIONS
readSensors() computeRisk()
No effects, no clock, no randomness.
DERIVED UI
6 readings + risk + protocol text
Recomputed every render.
The four consumers of that derived state
3D twin
Sensor beacons colour by status; labels show live values.
Telemetry charts
28-point rolling history, sampled on a 2 s clock.
Risk gauge
Score plus the three named driver contributions.
Protocol panel
Recommendation text selected by risk band.
Why it matters: state is never synced, only derived.
The same three numbers always produce the same six readings and the same score —
so any frame of the demo is exactly reproducible from three values.

## Slide 4
2 · The three simulator inputs
Everything the demo shows is a function of these three numbers.
Input
Meaning
Range
Step
Rest value
surge
Reservoir rise above normal operating level
0 → 15 m
0.5
0
pga
Peak ground acceleration at the abutment
0 → 0.45 g
0.01
0.02
spillwayGate
Gate opening — discharge capacity available
10 → 100 %
5
100
closure = 100 - spillwayGate
Gate opening is inverted into a closure percentage before it reaches any equation.
A fully open gate (100%) contributes exactly zero. A seized gate at 10% contributes 90 units of closure.
Rest state is not zero risk
PGA idles at 0.02 g (ambient microseismic background), so the dashboard never shows a dead-flat trace.
Sliders lock during a scenario
While a scripted scenario runs, the scenario clock owns the three inputs and the sliders go read-only.

## Slide 5
3 · The sensor network
Six instruments, each with a rest reading and two alarm thresholds.
ID
Instrument
Location
Unit
Base
Warn ≥
Crit ≥
P-01
Piezometer
Upstream Heel (EL 490 m)
kPa
242.4
270
300
P-02
Piezometer
Foundation Gallery (EL 510 m)
kPa
185.1
205
220
P-03
Piezometer
Downstream Toe (EL 480 m)
kPa
92.6
130
150
INC-04
Pendulum / Inclinometer
Crest Centre (Block 04)
mm
3.2
6.5
8.0
SF-02
Seepage Flow Gauge
Drainage Gallery G-02
L/min
14.2
20
25
WL-01
Water Level Radar
Reservoir Intake Tower
m
537.4
543
546
Base = the reading at rest: surge 0, pga 0, gate 100%. Thresholds are one-sided — every sensor here alarms on rising values only.
Instrument naming follows arch-dam practice, not embankment practice.
Heel / toe / foundation gallery / pendulum — the terminology a concrete double-curvature
arch dam would actually use on its instrumentation schedule.

## Slide 6
4 · The sensor response equation
One line of arithmetic produces every reading on screen.
value = base + surge × kSurge + pga × kPga + closure × kGate
linear superposition of three independent load cases
base
Rest reading
The instrument's value with the reservoir at normal level and no shaking.
surge × kSurge
Hydrostatic term
Reservoir rise in metres × that sensor's metres-of-surge sensitivity.
pga × kPga
Seismic term
Ground acceleration in g × that sensor's per-g sensitivity.
closure × kGate
Discharge term
Percent of gate closure × that sensor's per-percent sensitivity.
Then: value is rounded to the sensor's own decimal precision before display and comparison.

## Slide 7
5 · The sensitivity coefficients
Which loads each instrument actually responds to — and how strongly.
Sensor
kSurge (per m)
kPga (per g)
kGate (per %)
Dominant driver
P-01
8.5
150
0.15
Hydrostatic
P-02
5.2
90
0.10
Hydrostatic
P-03
2.4
60
0.08
Mixed
INC-04
0.4
25
0
Seismic
SF-02
1.8
30
0
Hydrostatic
WL-01
1.0
0
0.02
Hydrostatic
A zero means genuinely no coupling
INC-04 and SF-02 carry kGate = 0: crest deflection and gallery seepage do not respond to gate position in this model. WL-01 carries kPga = 0 — shaking does not move the reservoir surface.
WL-01's kSurge is exactly 1.0
By construction: reservoir level rises one metre per metre of surge. It is the one coefficient that is definitional rather than calibrated.
Piezometers dominate the seismic term
kPga of 150 at the heel means 0.45 g alone adds 67.5 kPa — more than half the distance from base to the critical limit.

## Slide 8
6 · Worked example — all six readings
Operating point: surge = 4.0 m, pga = 0.05 g, gate = 100% (closure = 0).
P-01 = 242.4 + 4.0 × 8.5 + 0.05 × 150 + 0 × 0.15
= 242.4 + 34.0 + 7.5 + 0.0 = 283.9 kPa → ≥ 270 warn, < 300 crit → WARNING
Sensor
Base
+ Surge
+ PGA
+ Gate
Value
Status
P-01
242.4
34.0
7.5
0.0
283.9 kPa
WARNING
P-02
185.1
20.8
4.5
0.0
210.4 kPa
WARNING
P-03
92.6
9.6
3.0
0.0
105.2 kPa
NORMAL
INC-04
3.2
1.6
1.25
0.0
6.1 mm
NORMAL
SF-02
14.2
7.2
1.5
0.0
22.9 L/min
WARNING
WL-01
537.4
4.0
0.0
0.0
541.4 m
NORMAL
Three sensors in warning, three normal — from a 4 m surge and near-negligible shaking. The spread is the point: because each instrument carries its own coefficients and its own thresholds, one operating point produces a mixed picture rather than six identical bars.
INC-04 sums to 6.05 and displays as 6.1 — rounding to the sensor's own precision happens before display and before the threshold test.

## Slide 9
7 · Status bands and bar fill
How a number becomes a colour.
status =
value ≥ critAt → 'critical'
value ≥ warnAt → 'warning'
otherwise → 'normal'
utilisation =
min(1.4, value / critAt)
Drives the fill fraction on each bar.
Two details worth knowing
Comparison happens after rounding
The value is rounded to the sensor's display precision first, then tested. What you read on screen is exactly what was compared — a reading shown as 270.0 kPa is in warning, with no hidden 269.97 behind it.
Utilisation is capped at 1.4, not 1.0
Bars keep growing past the critical limit so an overshoot stays visible, but stop at 140% so a runaway value cannot blow out the layout. A bar pinned at full width means ≥ 140% of critical.
Status drives colour everywhere at once: the sensor tile, its 3D beacon, and its label ring.

## Slide 10
8 · The risk score
A sum of named contributions, so the gauge can explain why it moved.
score = clamp( hydrostatic + seismic + discharge + 12 , 5 , 100 )
hydrostatic
surge × 3.8
0 → 57.0
Reservoir loading. The largest single contributor at full range.
seismic
pga × 140
0 → 63.0
Ground shaking. Steepest coefficient — 0.45 g alone exceeds the warning band.
discharge
closure × 0.35
0 → 31.5
Lost spillway capacity. Smallest contributor, but always present when gates are throttled.
baseline
12 (constant)
12
RISK_BASELINE — the standing risk of operating a dam at all. Never zero.
Sum at full range = 57 + 63 + 31.5 + 12 = 163.5, so the score saturates at 100 well before the sliders max out.

## Slide 11
9 · Risk bands and a worked score
Three bands, and the same operating point as slide 6.
score > 60
CRITICAL RISK
SEVERE STRESS
score > 28
ELEVATED RISK
WARNING
score ≤ 28
LOW RISK
STRUCTURALLY STABLE
At surge = 4.0 m, pga = 0.05 g, gate = 100%:
hydrostatic = 4.0 × 3.8 = 15.2
seismic = 0.05 × 140 = 7.0
discharge = 0 × 0.35 = 0.0
baseline = 12.0
score = 15.2 + 7.0 + 0.0 + 12.0 = 34.2 → > 28 → ELEVATED RISK — WARNING
The gauge shows the split, not just the total.
34.2 points made of 15.2 hydrostatic + 7.0 seismic + 0.0 discharge tells an operator to look at the reservoir, not the gates or the fault. That decomposition is the whole reason the score is a sum of named terms rather than a single opaque formula.

## Slide 12
10 · The recommended protocol
A lookup on the risk band — deterministic, not generative.
CRITICAL
score > 60
Open spillway gates to 100%. Dispatch structural team to inspect the downstream toe (P-03) and drainage gallery. Notify downstream settlements per Emergency Action Plan.
WARNING
score > 28
Hydrodynamic pressure elevated. Increase piezometric sampling to 1 s intervals, verify gallery drain flow at SF-02, and stage auxiliary spillway gates for release.
NORMAL
score ≤ 28
Structure stable under nominal hydrodynamic loads. No intervention required. Piezometric heads and crest deflection within design safety envelopes.
No language model is involved. The 'AI Recommended Protocol' panel selects one of three fixed strings.

## Slide 13
11 · The scenario engine
How a scripted event drives the sliders, the twin, the charts and the gauge from one clock.
1
Progress
p = elapsed / durationMs, clamped to 1. One requestAnimationFrame loop owns it.
2
Bracket
Find the keyframe pair a, b where a.at ≤ p ≤ b.at.
3
Normalise
raw = (p − a.at) / (b.at − a.at) — position between those two keyframes.
4
Ease
t = raw² × (3 − 2·raw) — smoothstep, so slider motion accelerates and settles.
5
Interpolate
Each of the three inputs is lerped from a to b using t, then pushed to state.
Events fire on threshold crossing:
while (fired < events.length
&& events[fired].at <= p)
→ append to the log, once only
Why smoothstep, not linear:
linear keyframes make the sliders
snap between poses. Smoothstep eases
in and out — it reads as real motion.

## Slide 14
12 · The three scenarios
Each one exercises a different term of the risk equation.
Scenario
Premise
Runtime
Peak load
Camera
Events
Flood Event
1-in-500-year inflow, staged gate response
26 s
surge 15.0 m
WL-01
8
Seismic Event
M6.4 near-field rupture, aftershock sequence
22 s
pga 0.38 g
INC-04
8
Gate Malfunction
Radial gate seizure during high inflow
20 s
gate 10%
SF-02
7
What each one is designed to show
Flood
Drives the hydrostatic term to its ceiling. Gates stage down 100 → 75 → 45 → 30% as capacity saturates, then reopen fully at p = 0.88 for drawdown. Ends with the structure recovered.
Seismic
Spikes the seismic term to 0.38 g at p = 0.12, decays, then a second 0.29 g aftershock at p = 0.42. Surge barely moves — this scenario isolates INC-04 crest deflection.
Gate
Holds pga flat and collapses the gate to 10%, so the discharge term and a slow surge climb carry the whole score. Recovery only comes at p = 0.86 when the gate is freed.
All three end in a recovered state — the demo is designed to close on a stable structure, not a failure.

## Slide 15
13 · Telemetry sampling and the trace jitter
The one place the demo is deliberately non-deterministic.
2 s
Sample interval
28
Points retained
56 s
Visible window
±0.075%
Jitter amplitude
jitter = (random() − 0.5) × max(0.05, value × 0.0015)
sample = round(value + jitter, decimals)
Why add noise at all
A pure model produces a perfectly flat line when nothing moves. Real instruments never do. The jitter is cosmetic — it makes an idle trace look like an instrument rather than a constant.
It never changes a status
Jitter is applied only to the charted history. Sensor tiles, statuses, the risk score and the 3D twin all read the clean deterministic value. Noise can never trip an alarm.
The floor matters
max(0.05, …) keeps a visible wiggle on small readings — INC-04 at 3.2 mm would otherwise jitter by ±0.0024 mm and round away to a flat line.

## Slide 16
14 · The 3D twin
What is rendered, and what is only representative.
Driven by the model
• Beacon colour — normal / warning / critical per sensor status
• Label text — live value and unit, updated every render
• Selection ring and camera focus — follows the selected sensor
• Scenario camera — each scenario frames its own focus sensor
Representative geometry only
• Arch shell, gorge walls and crest road are modelled, not surveyed
• Sensor positions are plausible placements, not as-built coordinates
• Internal zoning (grout curtain, gallery, monolith) is illustrative
• No structural solver — nothing here is computed from geometry
Zoom-aware labels: scale = lerp(1.3, 0.45, smoothstep(distance, 8, 30))
Labels sit at 1.3× when the camera is at its closest dolly stop and shrink to 0.45× at the widest,
so readings stay legible up close without the label swarm covering the dam in the wide shot.
Rendered with react-three-fiber over WebGL. Labels are DOM elements positioned in 3D, not textures.

## Slide 17
15 · What this model is not
Read this before quoting any number from the demo.
It is not a structural analysis
No finite element method, no seepage solver, no material properties. Sensor responses are linear coefficients chosen to behave plausibly, not derived from the geometry on screen.
Superposition is assumed
The three load cases add independently. Real coupling — surge changing the seismic response, seepage lagging behind reservoir level — is not represented. There is no time lag anywhere in the model.
The risk score is not a standard
The 3.8 / 140 / 0.35 weights and the 28 / 60 band edges are demonstration values. They are not traceable to ICOLD, to any national dam safety guideline, or to a calibrated fragility curve.
The dam is fictional
Demo Dam is not a real facility. Elevations, thresholds and base readings are invented to be self-consistent and realistic in shape, nothing more.
What it does demonstrate: the interaction model, the data flow, and the operator experience — end to end.

## Slide 18
REPRODUCE ANY FRAME
Three numbers. That's the whole state.
surge · pga · spillwayGate
Set those three sliders and every reading, every status colour, every bar fill and the risk score reproduce exactly. Nothing on the dashboard is stored, streamed, or remembered — it is all recomputed from those three values on every render.
Source of truth: src/lib/damModel.ts · Deck generator: create_technical_presentation.py
SU YAPI Engineering & Consulting · Para Sidara
Demo Dam (Block 04) — demonstration dataset, not live field telemetry.